## Slide 1
Hybrid PCA representation of CrIS spectra
David Tobin1, Joe Taylor1, Flavio Iturbide-Sanchez2, Liam Gumley1, Graeme Martin1, Michelle Loveless1, Bob Knuteson1, Hank Revercomb1
1 Cooperative Institute for Meteorological Satellite Studies, Space Science and Engineering Center,
University of Wisconsin-Madison
2 NOAA, NESDIS, STAR
EUMETSAT 2022
19-23 September 2022
Brussels, Belgium

## Slide 2: Outline
Introduction / Methodology
Compression and Noise filtering
Example assessments
Next steps
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022

## Slide 3
Introduction
The EUMETSAT Hybrid PCA technique
  e.g.: Hultberg et al. 2017
  Currently available for IASI, and will be used for IASI-NG and MTG-IRS
Benefits
  Data compression, up to ~50x
    CrIS data accessibility
    Preparing for future sensors
  Random Noise Filtering
  Rare Events Detection (RED)
SNPP mission
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022

## Slide 4
CrIS Hybrid PCA Methodology
Determine a set of global PCs, “PCglobal”
Based on a large representative set of spectra
The leading nPCsglobal (150) global PCs are retained
These global PCs are “static” and distributed to users (and the global mean spectrum Radglobal)
For any given granule of SCRIF data
(1) Compute Coefficients for the global PCs, “Cglobal”
(2) Compute “Local PCs” based on the global reconstruction residuals of this granule, “PClocal” and the corresponding coeficients “Clocal” and retain these for the leading nPCslocal (10) local PCs (and the local mean residual spectrum Reslocal)
(3) Save Cglobal, PClocal, Clocal, Reslocal to a file for each granule
Final Reconstructed Radiances:
RadRec = ( PCglobal Cglobal + Radglobal ) + ( PClocal Clocal + Reslocal )
[2223xNrec] [2223x150] [150xNrec] [2223x1] [2223 x 10] [10 x Nrec] [2223 x 1]
Global Local
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022
Notes: Ma

## Slide 5
CrIS Hybrid PCA Methodology (Cont.)
Other considerations:
  All three spectral bands combined
  All nine FOVs combined
  150 global PCs and 10 local PCs
  Sensor independent or sensor dependent global PCs (TBR)
  Noise Normalization (FOV independent)
  Scaled integer representation of PC scores combined with NetCDF integer compression
  PC representation Quality indicators
  Individual Outliers
  Local granule size
  Missing spectral bands
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022

## Slide 6
Global Training
global PCs
Based on a large representative set of spectra
For each sensor (SNPP and NOAA20) currently using spectra from 1 year of data (March 2018 to March 2019)
with latitude weighting
~671M spectra per sensor
PCs computed from the SVD of covariance of the radiance ensemble
Covariance matrices of subsets (single days) of the ensemble combined into a covariance matrix for the entire ensemble following:
  Pebay, P., 2008, Formulas for Robust, One-Pass Parallel Computation of Covariances and Arbitrary-Order Statistical Moments: Sandia Report
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022

## Slide 7
1
10
71
80
141
150
Global PCs
Local PCs
For a randomly selected SCRIF granule
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022
Example PCs

## Slide 8
mW/(m2 sr. cm-1)
mW/(m2 sr. cm-1)
Scaled Integer representation of PC scores
Example reconstructed radiance differences
32 Bit Float vs 16 Bit Unsigned Integers
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022
Mean
STDEV

## Slide 9
PC reconstruction Quality indicators
*Following Hultberg et al: ‘IASI PC compression – Searching for signal in the residuals’ 13886-iasi-pc-compression-searching-sinal-residuals.pdf
and Hultberg, 2009, ‘IASI Principal Component Compression (IASI PCC) FAQ’ pdf_ipcc_faq.pdf
“De-trended” reconstruction RMS scores for each footprint and spectral band, for Global-only and Hybrid reconstructions
Corresponding Quality Flags
Original radiances for “Individual outlier” spectra, when identified, included in output PC files
Useful for “rare event” identifications
Example for 20220101 Mt. Etna eruption NOAA20 data (using Global-only PC reconstruction for demonstration)
Radiance RMS versus integrated radiance for MidWave band, by FOV:
Not de-trended
De-trended

## Slide 10
Compression (SDR example)
Radiances from a 4 scan line CrIS granule (1080 spectra): 9,551,520 bytes
Global PCs (150 PCs, 1 time transfer): 2,653,200 bytes
Global Coefs (per granule): 648,000 bytes
Local PCs (10 PCs, per granule): 88,440 bytes
Local Coefs (per granule): 43,200 bytes
Per granule:
FSR SDR Radiances = 9,551,520 bytes
PC representation = 648,000 + 88,440 + 43,200 bytes = 779,640 bytes
PC/SDR x100 = 8.2% ... PC data volume is ~8 percent of SDR radiance data volume
SDR/PC = 12.3 … A factor of ~12 reduction in terms of data transfer expense and data storage
And an additional compression of 2 to 4x, from scaled integer representation of the PC scores, gives total compression of up to ~50x
This large reduction is due to the lossy noise reduction/compression from the PCA …
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022

## Slide 11: Random Noise Filtering Example reconstruction residuals 900 cm-1 radiances 20210413 NOAA-20 data
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022
mW/(m2 sr. cm-1)
mW/(m2 sr. cm-1)
Original Radiance
Original minus Reconstructed Radiance
mW/(m2 sr. cm-1)
normalized counts

## Slide 12: Random Noise Filtering Example reconstruction residuals 20210413 NOAA20 radiances ~75% random Noise reduction [sqrt(160/2223)] produces data with FOV independent random noise levels
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022
Longwave
Midwave
Shortwave
spectra
residuals
Mean residual
STDEV residual
mW/(m2 sr. cm-1)
mW/(m2 sr. cm-1)
mW/(m2 sr. cm-1)

## Slide 13
~165Mb
~4Mb
  Example 40 scan line file
  Image of 900 cm-1 radiances:
  Color scale is 20 to 100 mW/(m2sr. 1/cm)
Original Radiances
PC Representation
Data Compression and Random Noise Filtering
  Channel difference image:
  900 cm-1 minus 900.625 cm-1:
  Color scale is -0.3 to 0.3 mW/(m2sr. 1/cm)

## Slide 14
Example Assessment: Spectral Inter-FOV Analysis
Original Radiances
Reconstructed Radiances
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022

## Slide 15
Example Assessment: Radiometric Inter-FOV Analysis
Original Radiances
Reconstructed Radiances
FOV 1 FOV 2 FOV 3
FOV 1 FOV 2 FOV 3
FOV 4 FOV 5 FOV 6
FOV 4 FOV 5 FOV 6
FOV 7 FOV 8 FOV 9
FOV 7 FOV 8 FOV 9
wavenumber
wavenumber
wavenumber
wavenumber
wavenumber
wavenumber
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022

## Slide 16
Example Assessment: Mt. Etna SO2 plume on 23 Feb 2021
DBT(K), 1345.625 cm-1 minus 1335 cm-1
Original Radiances
Reconstructed Radiances
Plume
Near plume
Local PCs and Local PC scores
10
9
8
7
6
5
4
3
2
1
1 2 3
4 5 6
7 8 9
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022
colorscale is -4 to +0.5 K

## Slide 17
Example Assessment: C2H2 from Australian wild fires 1 Jan 2020
Radiance Reconstruction RMS over 728 to 732 cm-1
Example Fire plume spectra
Global PC reconstruction residuals:
Hybrid PC reconstruction residuals:
Global PC
Hybrid PC
Following Sarah Pipien et al. “Principal component analysis of IASI measurements for the analysis of performances of L0 & L1 processing”
Ethyne, C2H2
HCN
Ethene, C2H4
mW/(m2 sr. cm-1)

## Slide 18
Example Assessment: Australian wild fires 1 Jan 2020 cont.
Radiance Reconstruction RMS
C2H2 C2H4 HCN
728-732 1/cm 948-952 1/cm 711-714 1/cm
Original - Global
Global - Hybrid
Original - Hybrid
mW/(m2 sr. cm-1)

## Slide 19: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-15

## Slide 20: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-15

## Slide 21: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-16

## Slide 22: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-16

## Slide 23: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-17

## Slide 24: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-17

## Slide 25: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-18

## Slide 26: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-18

## Slide 27: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-19

## Slide 28: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-19

## Slide 29: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-20

## Slide 30: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-20

## Slide 31: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-21

## Slide 32: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-21

## Slide 33: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-22

## Slide 34: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-22

## Slide 35: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-23

## Slide 36: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-23

## Slide 37: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-24

## Slide 38: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-24

## Slide 39: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-25

## Slide 40: Hunga Tonga, Local contribution @ 1653.125 cm-1
2022-01-25

## Slide 41
Next Steps
(TBR) Implement as a prototype L1B project product, and create Worldview display for Rare Event Detection (RED)
  Define product files, Documentation, provide software utilities, facilitate test users
Continue to assess the PC product quality
  A more comprehensive assessment using more data
  Including reconstructed radiances, quality variables, and compression
  Inputs from other groups (retrievals, NWP)
(TBR) Implement CrIS HPC software within the Community Community Satellite Processing Package (CSPP)
  Define product files, Documentation, provide software utilities, facilitate test users
NASA Sounder Discipline Team telecon, D. Tobin, 25 Jan 2023

## Slide 42
Huang et al., 2001. Application of Principal Component Analysis to High-Resolution Infrared Measurement Compression and Retrieval. Journal of Applied Meteorology. 40. 365-388. 10.1175/1520-0450(2001)040<0365:AOPCAT>2.0.CO;2.
Antonelli et al., 2004, A principal component noise filter for high spectral resolution infrared measurements. Journal of Geophysical Research. 109. 10.1029/2004JD004862.
Turner et al., 2006. Noise Reduction of Atmospheric Emitted Radiance Interferometer (AERI) Observations Using Principal Component Analysis, Journal of Atmospheric and Oceanic Technology, 23(9), 1223-1238.
Tobin et al., 2007. Hyperspectral data noise characterization using principal component analysis: application to the atmospheric infrared sounder, J. Appl. Rem. Sens. 1(1) 013515 doi: 10.1117/1.2757707
Zavyalov et al., 2011. Preflight assessment of the Cross-track Infrared Sounder (CrIS) performance. Proc. SPIE Eur. Atmos. Remote Sens.. 8176. 10.1117/12.897674.
Serio et al., 2015. Infrared atmospheric sounder interferometer radiometric noise assessment from spectral residuals. Appl Opt. 2015 Jul 1;54(19):5924-36. doi: 10.1364/AO.54.005924. PMID: 26193134.
Hultberg et al., 2017. Local or global? How to choose the training set for principal component compression of hyperspectral satellite measurements: a hybrid approach, Proc. SPIE 10423, Sensors, Systems, and Next-Generation Satellites XXI, 104231G (29 September 2017); doi: 10.1117/12.2278349.
Lee et al., 2019. HIRAS noise performance improvement based on principal component analysis. Appl Opt. 2019 Jul 10;58(20):5506-5515. doi: 10.1364/AO.58.005506. PMID: 31504021.
Serio et al., 2020. Characterization of the Observational Covariance Matrix of Hyper-Spectral Infrared Satellite Sensors Directly from Measured Earth Views. Sensors (Basel). 2020 Mar 9;20(5):1492. doi: 10.3390/s20051492. PMID: 32182769; PMCID: PMC7085552.
Tremblay et al., 2022, "Radiometric Noise Assessment of the Cross-Track Infrared Sounder on the NOAA-20 Satellite," in IEEE Transactions on Geoscience and Remote Sensing, vol. 60, pp. 1-15, 2022, Art no. 5506615, doi: 10.1109/TGRS.2021.3083137.
--
EUMETSAT, 2019. Release of simulated MTG IRS Level 1B data package. https://www.eumetsat.int/simulated-mtg-irs-l1b-dataset
EUMETSAT, 2021. Changes to PC compressed IASI L1C data. https://www.eumetsat.int/changes-pc-compressed-iasi-l1c-data
References

## Slide 43: Principal Component Analysis (PCA) basics
A radiance spectrum with spectral channels can be written as a linear combination of scalar coefficients and Principal Components plus the ensemble mean spectrum:
=
where C and U can be determined from Single Value Decomposition of the radiance ensemble.
are ordered such that explains the most variance and explains the least, and a reconstructed spectrum can be computed from a relatively small number of Principal Components, :
=
https://www.analyticsvidhya.com/blog/2020/12/an-end-to-end-comprehensive-guide-for-pca/
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022

## Slide 44
Global Training
Example assessment of combined covariance
Percentage difference scale: < 1e-10

## Slide 45
Example Assessment: Isoprene C5H8 detection (?)
DBT(K), 893.75 cm-1 minus 898.125 cm-1
Original Radiances
Reconstructed Radiances
Sample spectra with Low, Medium,and High amounts
Original Radiances
Reconstructed Radiances
Difference
Hybrid PCA representation of CrIS spectra, D. Tobin, EUMETSAT 2022
mW/(m2 sr. cm-1)
mW/(m2 sr. cm-1)
mW/(m2 sr. cm-1)

## Slide 46
The Tarfaya Oil Shale deposit
HNO2 Nitric Acid
Example BT spectra
Local PC capturing
HNO2 signature
Corresponding local PC scores
wavenumber
wavenumber
BT (K)