## Slide 1
Feasibility and Applications of Retrieving Oil and Gas Ethane Emissions from Space
Colby Francoeur1-3, Brian McDonald1, Jian He1,2, Colin Harkins1,2, Daven Henze3
  NOAA Chemical Sciences Laboratory, Boulder, CO USA
  Cooperative Institute for Research in Environmental Sciences, University of Colorado, Boulder, CO USA
  Department of Mechanical Engineering, University of Colorado, Boulder, CO USA
NASA Sounder Discipline telecon
May 15th, 2024

## Slide 2
Petroleum and Natural Gas Growing Source of US Energy Mix
Projected to grow
~30% by 2050
Projected to increase,
then decrease by 2050
(little change)
Domestic energy production
~95% of US consumption
US Energy Information Administration (Monthly Energy Review, 2024)
US Primary Energy Consumption (1950-2023)
Quadrillion BTUs

## Slide 3
VOC Correlation
Francoeur et al. (Environ. Sci. Technol., 2021)

## Slide 4
Research Objectives
    Demonstrate ability to retrieve O&G C2H6 from Cross-track Infrared Sounder (CrIS)
  Evaluate in conjunction with 2015 O&G field campaign
  Compare CrIS trends with expected production and emission intensity trends
CrIS constructed to measure atmospheric temperature, pressure and moisture profiles, but also relevant for key atmospheric composition species
Onboard NOAA-20 since 2017 and Suomi-NPP since 2011

## Slide 5
HITRAN absorptions between 821 and 824 cm-1
Gordon et al. (2022)

## Slide 6
CrIS Ethane Brightness Temperature Difference (ΔBT)
ΔBT=0.5*(BT821.25 +BT823.125 - BT821.875 - BT822.5)
Higher ΔBT→ more absorption
Eliminate errors due to clouds, surface temperature, emissivity etc.
Notes: Strength – removes a lot of systematic errors
Weakness- relying on only a few weak signals

## Slide 7
Plotted Brightness Temperature Difference
NASA Community Long-term Infrared Microwave Coupled Atmospheric Product System (CLIMCAPS) radiances corrected for clouds
Monarrez et al. (CLIMCAPS User Guide, 2021)

## Slide 8
VLIDORT Modeling
CLIMCAPS retrieved Variables:
T(p), q(p), CO2(p),CH4(p) Reflectance
Solar and Satellite Angles
Vector Linearized Discrete Ordinate
Radiative Transfer (VLIDORT)
Modeled ΔBT without C2H6
Simulated Radiance
Satellite Radiance

## Slide 9
          4.8%
          100%
          20%
          60.8%
Model ΔBTnon-ethane
WRF-Chem Column
OBS-Model ΔBTethane
OBS ΔBTtotal
Molec/cm2
Removing Interferences from Observations

## Slide 10
WRF-Chem modeling during SONGNEX
Simulated in WRF-CHEM (12 km x 12 km)
March 28th-April 26th 2015

## Slide 11
Ethane Profile
Averaging Kernel

## Slide 12
Choosing which AK to apply
H
M
L

## Slide 13
Choosing which AK to apply

## Slide 14
Next Steps and Impact
    Compute averaging kernel and apply to model
      Computationally expensive
      Determine skill of instrument
    Improved ΔBT could be used to get the trends of C2H6 over OG fields
      2012-Present, as well as guaranteed for 10+ years
      C2H6 is important as a tracer and ozone precursor
      Improving understanding of C2H6 trend helps assess other OG emissions

## Slide 15
Questions?
Contact: Colby.Francoeur@noaa.gov