## Slide 1: AIRS Science Team Sounder SIPS Status and Plans
Steven Friedman and Ruth Monarrez Jet Propulsion Laboratory, California Institute of Technology
Bruce Vollmer and Mike Theobald
NASA Goddard Space Flight Center
Christopher Barnet
Science and Technology Corporation
California Institute of Technology
September 14, 2016
© 2016. All rights reserved.

## Slide 2: A word about the Sounder SIPS
The Sounder SIPS consists of two elements:
  Science Integration & Computing – JPL
    Integration of code from Science Teams
    Development of production-level PGEs and research products
    Documentation
  Data Production / OPS – GSFC GES DISC
    Production of all official NASA sounder products from SNPP
    Archive of all products
Data Archive
  Located at the GES DISC
Points of Contact
  JPL – Steve Friedman and Ruth Monarrez
  GES DISC – Bruce Vollmer and Mike Theobald

## Slide 3: External Relationships
The Sounder SIPS works closely with:
  The SNPP Sounder Science Team
    Overall direction coordinated through the Sounder Science Team lead, Chris Barnet
    Coordination support through our Sounder Science Team liaison, Eric Fetzer
  The AIRS Project
    Algorithm and code sharing (when it makes sense)
    Shared resources, including staff
  The SNPP Level 1 Algorithm teams
    CrIS: University of Wisconsin – Graeme Martin
    ATMS: Jet Propulsion Laboratory – Bjorn Lambrigtsen
  Guidance and ESDIS Liaison
    Alfreda Hall – ESDIS Project

## Slide 4: Functional Interfaces

## Slide 5: Requirements Summary
Production of Level 1, 2 and 3 data products from SNPP Sounder instruments: ATMS and CrIS (CrIMSS)
  Level 1 ATMS and CrIS PGEs
  Integration of Level 2 PGEs from SNPP Sounder Science Team – Five unique product streams at JPL (demonstration activity) – One Level 2 product stream at GES DISC (routine operations)
  Level 3 CrIMSS daily, multi-day, monthly – developed at JPL
  CalSub, Simultaneous Nadir Observations and Match-up – developed at JPL
Develop and/or integrate PGEs listed above
Support the Science Team in data validation activities
Document and deliver source code, executables, user guide and ATBDs to the GES DISC for long-term storage and access
Produce all standard products and archive at DAAC
Notes: Analysis Match-up? Add it here?

## Slide 6: Data Products Interfaces

## Slide 7: Sounder SIPS Product Specification
Sounder SIPS Product Specification
  All products will be netCDF-4, formatted to conform with ACDD1, CF2, and ISO metadata standards
  Granule Sizes:
    Level 1B ATMS and CrIS: 6-minute granules
    Level 2: 6-minute granules, matching CrIS footprint
    Level 3 Daily: Gridded global data
      Two groups: ascending and descending
      1º x 1º gridded data.
    Level 3 Multi-day and Monthly products follow same pattern like daily
    SNO and CalSub will continue to be RTP33 format temporarily – we currently plan to convert to netCDF-4 within the next year
1Attribute Convention for Dataset Discovery
2Climate and Forecast
3RTP3 developed by the Sounder PEATE
Notes: ACDD = Attribute Convention for Dataset Discovery

## Slide 8: Sounder SIPS Product Release
Sounder SIPS Product Release Specifications
  All Sounder SIPS products will be produced in accordance to the NASA data policy
    Rapid release of all products
    No sequestration of products for science team-only use
Notes: ACDD = Attribute Convention for Dataset Discovery

## Slide 9: Sounder SIPS Data Flow

## Slide 10: Sounder SIPS CrIS ATMS Milestones
Level 1 ATMS
  Beta release – March 2016 (for Science Team evaluation – not publicly released)
  V1 Release – January 2017 (public release*)
Level 1 CrIS (normal spectrum… “classic CrIS”)
  Beta release – March 2016 (for Science Team evaluation – not publicly released)
  V1 Release – January 2017 (public release*)
ATBD
  ATMS: Review version delivered to NASA HQ in June 2014
  CrIS: Initial version delivered to JPL Feb 2016
*Publically released data will be accessible via GES DISC data ordering tools.

## Slide 11: Sounder SIPS CrIS Full Spectrum
Level 1 CrIS (full spectrum… “new CrIS”)
  Pre-release products – January 2017 (publically accessible)
    netCDF-4 formatted to conform with ACDD, CF, and ISO metadata standards – but may have some fill-fields
    Sample data collection should be of sufficient quantity and quality to support upcoming ROSES proposals
    Some format changes are expected as development continues!
  Public Release – January 2018
ATBD
  CrIS: an updated version will be available around January 2017
*Publically released data will be accessible via GES DISC data ordering tools.

## Slide 12: Sounder SIPS L2 Milestones
Baseline Level 2 (using Susskind’s joint-AIRS/SNPP retrieval code)
  Internal demonstration tests at JPL – Fall 2016
  V1 release to GSFC GES DISC – Spring 2017
  Public release V1 Level 2 products – Spring 2017
Internal production of other L2 retrievals TBD, pending schedule and plans by Science Team
  ATMS (microwave-only) Retrieval – Lambrigtsen
  CrIMSS – Barnet
  CrIMSS – Moncet
  NH3 (post-processor) – Cady-Pereira and Worden
  CO (post-processor) – Cady-Pereira and Worden

## Slide 13: Near-Real-Time Processing
No near-real-time processing is planned.
  Community will rely on use of NOAA NRT products
    Primary NRT customers are NOAA
    NASA community expressed no interest in NRT sounder products
Sounder SIPS/Science Team will focus on development of “climate quality” products
Sounder SIPS will respond to community needs for NRT products when and if they are requested.

## Slide 14: Plans for Other PGEs:
Level 3 – gridded summaries of retrieval products, grouped into ascending and descending, 1x1-degree cells
  Daily
  Multiday
  Monthly
Products being upgraded (to netCDF-4) from PEATE:
  Simultaneous Nadir Observations (SNO)
  Calibration Subsets (CalSub)
Overall PGE development strategy (for all PGEs)
  Sounder Science Team members own their own code
  Sounder SIPS will use science code as delivered.
  Sounder Science Team is responsible for validation activities.

## Slide 15: Yes Bill, they are not as cute when they get older!

## Slide 16: …but, the grandkids sure are!

## Slide 17: Questions?

## Slide 18: Backup Slides

## Slide 19: Sounder SIPS Software Flow – ATMS L1

## Slide 20: Sounder SIPS Software Flow – CrIS L1

## Slide 21: Sounder SIPS Organization (JPL)

## Slide 22: Sounder SIPS Points of Contact (GSFC)
Goddard Earth Sciences DISC
Steve Kempler, Manager
Engineering
Mission Support
Operations
Operations
Gary Alcott, Manager
Jecue Dechateu, Production Lead
Beth Stetzler, Archiver
Science Support
SW Engineering
Sys Admin
Mission Support
Bruce Vollmer, Manager
Mike Theobald, Lead Engineer
Dan Trang, Ancillary Data Support

## Slide 23: New NASA Science Teams and SIPS for SNPP
The Sounder Science Team selected from ROSES A.29:
  Chris Barnet – Team Lead (Standard L2 Products – CrIMSS) Development and validation of a community hyper-spectral infrared microwave Earth retrieval algorithm: CHIMERA
  Hartmut Aumann (L1 product analysis) Analysis of the AIRS and CrIS radiometric calibration under cloudy conditions and error propagation into environmental variables
  Jean-Luc Moncet and Vivienne Payne (Standard L2 Products – CrIMSS) Refined Atmosphere Data Products from CrIS and ATMS
  Joel Susskind (Standard L2 Products – CrIMSS) Analysis of CrIS/ATMS using an AIRS Version 6-like retrieval algorithm
  Karen Cady-Pereira and Helen Worden (Specialized L2 Product) Developing retrieval algorithms for NH3 and CO from NPP CrIS measurements
  Bjorn Lambrigtsen (Standard L2 Products – ATMS) Microwave sounder Earth System Data Records

## Slide 24: Sounder SIPS Hardware (JPL)

## Slide 25: Sounder SIPS Hardware (GES DISC)
64 CPU 252 GB
EDOS
F/C
Attached
RAID
VM with 8 CPU, 8 GB
SNPP L0 Archive
Primary
Archive for
ATMS and
CrIS L0
F/C
Attached
RAID
SNPP Production Cluster
Sounder
Production
Cluster
(and L0 Backup
Archive)
F/C
Attached
RAID
VM with 12 CPU 24 GB
SNPP Sounder Archive
Primary
Archive for
ATMS and CrIS
L1, L2 and L3
JPL
U Wisc
64 CPU 252 GB
64 CPU 252 GB
planned
64 CPU, 252 GB
deployed

## Slide 26: Sounder SIPS Data Products
Short Name (DOI) | Instrument | Collection Summary | Avg Gran Size (MB) | Gran/ Day | Daily Tansfer (MB/Day)
Level 1 |  |  |  |  | 
SNPPATMSL1A | ATMS | SuomiNPP ATMS Level 1A | 6 | 240 | 1440
SNPPATMSL1B | ATMS | SuomiNPP ATMS Level 1B | 9 | 240 | 2160
SNPPCrISL1A | CrIS | SuomiNPP CrIS Level 1A |  | 240 | 
SNPPCrISL1BLSR | CrIS | SuomiNPP CrIS Level 1B Low Spectral Resolution | 246 | 240 | 59,040
SNPPCrISL1BFSR | CrIS | SuomiNPP CrIS Level 1B Full Spectral Resolution |  | 240 | 
Level 2 |  |  |  |  | 
SNPPATMSL2 | ATMS | SuomiNPP ATMS Level 2 |  | 240 | 
SNPPCrIMSSL2A | CrIS/ATMS | SuomiNPP CrIMSS Level 2 Atmospheric and Environmental Research, Inc. |  | 240 | 
SNPPCrIMSSL2G | CrIS/ATMS | SuomiNPP CrIMSS Level 2 Goddard Space Flight Center |  | 240 | 
SNPPCrIMSSL2S | CrIS/ATMS | SuomiNPP CrIMSS Level 2 Science and Technology Corporation |  | 240 | 

## Slide 27: Sounder SIPS Data Products (con’t)
Short Name (DOI) | Instrument | Collection Summary | Avg Gran Size (MB) | Gran/ Day | Daily Tansfer (MB/Day)
Level 3 |  |  |  |  | 
SNPPATMSL3D1 | ATMS | SuomiNPP CrIMSS Level 3 Gridded Daily ATMS | 140 | 1 | 
SNPPATMSL3D8 | ATMS | SuomiNPP CrIMSS Level 3 Gridded 8Day ATMS |  | 1/8 | 
SNPPATMSL3M1 | ATMS | SuomiNPP CrIMSS Level 3 Gridded Monthly ATMS |  | 1/30 | 
SNPPCrIMSSL3D1NSRA | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Daily Atmospheric and Environmental Research, Inc. | 141 | 1 | 
SNPPCrIMSSL3D8NSRA | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded 8Day Atmospheric and Environmental Research, Inc. |  | 1/8 | 
SNPPCrIMSSL3M1NSRA | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Monthly Atmospheric and Environmental Research, Inc. |  | 1/30 | 
NSRSNPPCrIMSSL3D1G | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Daily Normal Spectral Resolution Goddard Space Flight Center |  | 1 | 
SNPPCrIMSSL3D8NSRG | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded 8Day Normal Spectral Resolution Goddard Space Flight Center |  | 1/8 | 
SNPPCrIMSSL3M1NSRG | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Monthly Normal Spectral Resolution Goddard Space Flight Center |  | 1/30 | 
SNPPCrIMSSL3D1NSRS | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Daily Normal Spectral Resolution Science and Technology Corporation (STC) |  | 1 | 
SNPPCrIMSSL3D8NSRS | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded 8Day Normal Spectral Resolution Science and Technology Corporation (STC) |  | 1/8 | 
SNPPCrIMSSL3M1NSRS | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Monthly Normal Spectral Resolution Science and Technology Corporation (STC) |  | 1/30 | 
SNPPCrIMSSL3D1FSRA | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Daily Full Spectral Resolution Atmospheric and Environmental Research, Inc. |  | 1 | 
SNPPCrIMSSL3D8FSRA | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded 8Day Full Spectral Resolution Atmospheric and Environmental Research, Inc. |  | 1/8 | 
SNPPCrIMSSL3M1FSRA | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Monthly Full Spectral Resolution Atmospheric and Environmental Research, Inc. |  | 1/30 | 
SNPPCrIMSSL3D1FSRG | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Daily Full Spectral Resolution Goddard Space Flight Center |  | 1 | 
SNPPCrIMSSL3D8FSRG | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded 8Day Full Spectral Resolution Goddard Space Flight Center |  | 1/8 | 
SNPPCrIMSSL3M1FSRG | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Monthly Full Spectral Resolution Goddard Space Flight Center |  | 1/30 | 
SNPPCrIMSSL3D1FSRS | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Daily Full Spectral Resolution and Technology Corporation (STC) |  | 1 | 
SNPPCrIMSSL3D8FSRS | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded 8Day Full Spectral Resolution Science and Technology Corporation (STC) |  | 1/8 | 
SNPPCrIMSSL3M1FSRS | CrIS/ATMS | SuomiNPP CrIMSS Level 3 Gridded Monthly Full Spectral Resolution Science and Technology Corporation (STC) |  | 1/30 | 

## Slide 28: Sounder Input Data Stream – Product Production Pipeline
PRIMARY PIPELINE
  GES DISC
  EDOS Level 0* ATMS and CrIS
      *Reconstructed ATMS and CrIS Level 0 from IDPS RDRs from University of Wisconsin for pre-EDOS data stream.
SECONDARY PIPELINE
  NOAA Star
  CrIS SDRs (full-spectrum product) - interim use
  CLASS
  CrIS SDRs (reduced-spectrum product) - interim use
  ATMS SDRs - interim use

## Slide 29: Sounder Input Data Stream – Correlative Products
Class FTP
Mission_Notices
Mission_Schedules
MetOp-A – (IASI_L1C, AMSUA_L1B, MHS_L1B, MIRS_L2_SND, MIRS_L2_IMG)
MetOp-B – (IASI_L1C, AMSUA_L1B, MHS_L1B, MIRS_L2_SND, MIRS_L2_IMG)
NOAA-N (AMSUA_L1B, MHS_L1B, MIRS_L2_SND, MIRS_L2_IMG)
NOAA-P (AMSUA_L1B, MHS_L1B, MIRS_L2_SND, MIRS_L2_IMG)
NOAA Star
NUCAPS Level 2
From AIRS Project at JPL
AIRS L1B, L2 & L3

## Slide 30: Sounder SIPS Auxiliary and Ancillary Data
NOAA NCEP
rtg_sst_g1
GFS [we get this from SD3E]
SD3E (& later from TBD)
RPM
CMO (Correction Matrix Operator)
fnmoc: nogaps (became NAVGEM on Aug 21, 2013) (3hr, 6hr 9hr, 12hr, 15hr, 18hr, 21hr 24hr data )
Two Line Elements (TLEs)
From AIRS archive at JPL
ECMWF
GFS