## Slide 1: NUCAPS EDR Product Performance: Ozone and Carbon Trace Gases
2016 NASA Sounder Science Team
Greenbelt, Maryland, USA
September 2016
Nicholas R. Nalli1,2, Q. Liu2, C. Tan1,2, A. Gambacorta3, C. D. Barnet3, X. Xiong1,2, F. Iturbide-Sanchez1,2, M. Wilson1,2, J. W. Smith3,4, et al.
1IMSG, Rockville, Maryland, USA
2NOAA/NESDIS/STAR, College Park, Maryland, USA
3STC, Columbia, Maryland, USA
4National Research Council, Washington, DC, USA

## Slide 2: Acknowledgments
The NOAA Joint Polar Satellite System (JPSS-STAR) Office (M. D. Goldberg, L. Zhou, et al.) and the NOAA/STAR Satellite Meteorology and Climatology Division (F. Weng and I. Csiszar).
SNPP Sounder Trace Gas EDR Validation Dataset collection
  Ozone
    NOAA AEROSE: V. R. Morris, E. Joseph, M. Oyola (HU/NCAS); D. Wolfe (NOAA/ESRL)
      AEROSE works in collaboration with the NOAA PIRATA Northeast Extension (PNE) project (R. Lumpkin, G. Foltz and C. Schmid), and is supported by the NOAA Educational Partnership Program (EPP) grant NA17AE1625, NOAA grant NA17AE1623, JPSS and STAR
    CalWater/ACAPEX: R. Spackman (STC); R. Leung (PNNL); C. Fairall, J. Intrieri (NOAA); N. Hickmon, M. Ritsche, A. Haruta, and the ARM Mobile Facility 2 (AMF2)
    World Ozone and Ultraviolet Radiation Data Centre (WOUDC) data contributors (DWD-GRUAN, & INPE, & KNMI, & NASA-WFF, & SMNA. http://www.woudc.org
    SHADOZ: Southern Hemisphere ADditional Ozonesondes (A. Thompson et al.)
  Carbon Trace Gases
    NASA Sounder Science Team: E. Olsen (for his expertise and assistance with the AIRS v6 EDR products), and T. Pagano, E. Fetzer (NASA/JPL)
    Total Carbon Column Observing Network (TCCON) (D. Wunch et al.) data were obtained from the TCCON Data Archive, hosted by the Carbon Dioxide Information Analysis Center (CDIAC), tccon.onrl.gov
STAR soundings team (past and present): A.K. Sharma, T. King, W. W. Wolf (STAR)

## Slide 3: Outline
JPSS Sounder Trace Gas EDR Cal/Val Overview
  JPSS Level 1 Requirements
  Validation Hierarchy recap
  NUCAPS Algorithm
    Offline v1.5 (operational emulation, CrIS nominal res)
    Offline v1.8.x (CrIS full-res)
NUCAPS IR Ozone Profile EDR Product Evaluation
  v1.5 (operational emulation)
    Global Focus Day
    Ozonesonde ensemble
  v1.8.1 (CrIS full-res)
    Global Focus Day
NUCAPS Trace Gas EDR Product Evaluation (Preliminary)
  Truth Datasets and Methodology
    AIRS Version 6
    TCCON
  NUCAPS (v1.5 and v1.8.3) versus AIRS v6
    Carbon Monoxide (CO)
    Methane (CH4)
    Carbon Dioxide (CO2)
  NUCAPS and AIRS versus TCCON
Summary and Future Work

## Slide 4: JPSS Sounder Trace Gas EDR Cal/Val Overview
NUCAPS EDR Product Performance: Ozone and Carbon Trace Gases

## Slide 5: JPSS Specification Performance Requirements CrIS Trace Gas EDR Uncertainty (O3, CO, CO2, CH4)
Source:
(L1RD, 2014, pp. 45-49)

## Slide 6: Validation Methodology Hierarchy (e.g., Nalli et al., JGR Special Section, 2013)
Numerical Model (e.g., ECMWF, NCEP/GFS) Global Comparisons
  Large, truly global samples acquired from Focus Days
  Useful for sanity checks, bias tuning and regression
  Limitation: Not independent truth data
Satellite Sounder EDR (e.g., AIRS, ATOVS, COSMIC) Intercomparisons
  Global samples acquired from Focus Days (e.g., AIRS)
  Consistency checks; merits of different retrieval algorithms
  Limitation: Similar error characteristics; must take rigorous account of averaging kernels of both systems (e.g., Rodgers and Connor, 2003)
Conventional RAOB Matchup Assessments
  WMO/GTS operational sondes launched ~2/day for NWP
  Representation of global zones, long-term monitoring
  Large samples after a couple months (e.g., Divakarla et al., 2006; Reale et al. 2012)
  Limitations:
    Skewed distribution toward NH-continents
    Mismatch errors, potentially systematic at individual sites
    Non-uniform, less-accurate and poorly characterized radiosondes
    RAOBs assimilated , by definition, into numerical models
Dedicated/Reference RAOB Matchup Assessments
  Dedicated for the purpose of satellite validation
    Known measurement uncertainty and optimal accuracy
    Minimal mismatch errors
    Atmospheric state “best estimates” or “merged soundings”
  Reference sondes: CFH, GRUAN corrected RS92/RS41
    Traceable measurement
    Uncertainty estimates
  Limitation: Small sample sizes and limited geographic coverage
  E.g., ARM sites (e.g., Tobin et al., 2006), AEROSE, CalWater/ACAPEX , BCCSO, PMRF
Intensive Field Campaign Dissections
  Include dedicated RAOBs, some not assimilated into NWP models
  Include ancillary datasets (e.g., ozonesondes, lidar, M-AERI, MWR, sunphotometer, etc.)
  Ideally include funded aircraft campaign using IR sounder (e.g., NAST-I, S-HIS)
  Detailed performance specification; state specification; SDR cal/val; case studies
  E.g., SNAP, SNPP-1,-2, AEROSE, CalWater/ACAPEX, JAIVEX, WAVES, AWEX-G, EAQUATE
Notes: SNAP – Suomi-NPP Aircraft validation Program (2015)

## Slide 7: NOAA Unique Combined Atmospheric Processing System (NUCAPS) Algorithm (1/2)
Operational algorithm
  Unified Sounder Science Team (AIRS/IASI/CrIS) retrieval algorithm (Susskind, Barnet and Blaisdell, IEEE 2003; Gambacorta et al., 2014)
  Global non-precipitating conditions
  Atmospheric Vertical Temperature , Moisture Profiles (AVTP, AVMP)
  Trace gas profiles (O3, CO, CO2, CH4)
  Validated Maturity for AVTP/AVMP, Sep 2014
Users
  Weather Forecast Offices (AWIPS)
    Nowcasting / severe weather
    Alaska (cold core)
  NOAA/CPC (OLR)
  NOAA/ARL (IR ozone, trace gases)
  TOAST (IR ozone)
  Basic and applied science research (e.g., Pagano et al., 2014)
    Via NOAA Data Centers (e.g., CLASS)
    Atmospheric chemistry research
    Universities, peer-reviewed pubs
NUCAPS IR O3
NUCAPS CO
NUCAPS CO2
NUCAPS CH4

## Slide 8: NOAA Unique Combined Atmospheric Processing System (NUCAPS) Algorithm (2/2)
NUCAPS Offline Code Versioning
  Version 1.5
    Offline emulation of current operational algorithm
    Runs on nominal CrIS spectral resolution data
  Version 1.8.1
    Offline experimental algorithm (used in ozone results)
    Runs on CrIS full spectral resolution data
    Uses conventional regression algorithm for the IR/MW first guess (as opposed to MW retrieval as in v1.7 full-res)
    Other upgrades
      Updated IR RTA bias correction coefficients (based on the best combination resulted after testing the use of several atmospheric states and trace gaseous profiles)
      IR emissivity threshold decreased from 1.05 to 1.0 in the temp_cris.nl namelist.
      Replaced the Taylor expansion to the Exponential formula in fasttau_co2.F
      As in v1.6: Updated MW bias correction; updated MW RTA model error coefficients; removal of MW channel 16
  Version 1.8.3
    Offline experimental algorithm (used in carbon trace gas results)
    Retrieval step changed from “RODCO2” (Rodgers) to “CO2”
    Optimized channels for CO2, CO and CH4 (damping is also changed)
    Optimized CH4 first guess

## Slide 9: IR OZONE Profile EDR
NUCAPS EDR Product Performance: Ozone and Carbon Trace Gases

## Slide 10: IR Ozone Profile EDR Validation (1/8) In Situ Truth Datasets
Collocated ozonesondes for O3 (ozone) profile EDR
  Dedicated Ozonesondes
    NOAA AEROSE (Nalli et al. 2011)
    CalWater/ACAPEX 2015
  Sites of Opportunity
    SHADOZ (Thompson et al. 2007)
      Costa Rica
      Hanoi
      Irene
      Java
      Natal
      Paramaribo
      Reunion
      American Samoa
    WOUDC
      STN043
      STN053
      STN107
      STN101
Notes: SHADOZ - Southern Hemisphere Additional Ozonesondes MOZAIC - Measurement of Ozone from Airbus in-Service Aircraft WOUDC - World Ozone and Ultraviolet Radiation Data Centre

## Slide 11: IR Ozone Profile EDR Validation (2/8) VALAR Ozonesonde-FOR Collocation Sample (n = 6024)
Geographic Histogram (Equal Area)
FOR Collocation Criteria: δx ≤ 125 km, −240 < δt < +120 min

## Slide 12: IR Ozone Profile EDR Validation (3/8) NUCAPS Offline (v1.5) versus Global Ozonesondes
Retrieval and A Priori First Guess
IR+MW Yield = 62.2%

## Slide 13: IR Ozone Profile EDR Validation (4/8) NUCAPS Offline (v1.5) versus Global Ozonesondes
Retrieval and ECMWF
IR+MW Yield = 62.2%

## Slide 14: IR Ozone Profile EDR Validation (5/8) NUCAPS Offline (v1.5) versus Global Ozonesondes
* Broad-Layer Statistics
(Per JPSS Level 1 Requirements)
IR+MW Yield = 62.2%

## Slide 15: IR Ozone Profile EDR Validation (6/8) NUCAPS Offline (v1.5) versus Global Focus Day 17-Feb-2015
IR+MW
First Guess
O3 Versus ECMWF
NUCAPS v1.5
Yield = 63.4%

## Slide 16: IR Ozone Profile EDR Validation (7/8) NUCAPS Offline (v1.8.1) versus Global Focus Day 17-Feb-2015
O3 Versus ECMWF
IR+MW
First Guess
NUCAPS v1.8.1
Yield = 70.1%

## Slide 17: IR Ozone Profile EDR Validation (8/8) NUCAPS Offline (v1.8.1) versus Global Focus Day 17-Feb-2015
* Broad-Layer Statistics
(Per JPSS Level 1 Requirements)
NUCAPS v1.8.1
Yield = 70.1%

## Slide 18: Carbon Trace Gases
NUCAPS EDR Product Performance: Ozone and Carbon Trace Gases

## Slide 19: Basic Methodology for Trace Gases (1/2)
Truth Datasets
  AIRS v6 standard trace gas EDRs (Cal/Val Method #2)
    Obtained for the global Focus Day 17 February 2015
    Total column integrated CO and CH4
    Offline v6 runs for CO2 were made available to us courtesy of Ed Olsen (JPL AIRS Science Team)
    Provides global assessment
  Total Carbon Column Observing Network (TCCON) (Wunch et al. 2011)
    Global network of ground-based FTS that accurately measure total column abundances of CO2, CO, CH4, N2O trace gases
    Provides independent “spot checks” for verifying NUCAPS and AIRS at the TCCON station locations

## Slide 20: Basic Methodology for Trace Gases (2/2)
For NUCAPS CO, CH4, profile EDRs on 100 RTA layers are integrated to obtain total column abundances (molecules/cm2) (e.g., Nalli et al. 2013)
For NUCAPS CO2, stats are performed simply for atmospheric column averages (in PPMV)
TCCON CO, CH4 (in dry mole fractions, ppm) are converted to total column abundance Σi (molecules/cm2) using the following formula
where xi is the TCCON-measured dry mole fraction for species i, and Σw is the H2O column abundance (provided by NUCAPS retrieval).
NUCAPS and AIRS for 17 February 2015 Focus Day are divided into ascending (ASC) and descending (DES) orbits
Linear interpolations of FOR (lat/lon) are performed to create one-to-one correspondence of collocation data points
  AIRS CO, CH4 interpolated to NUCAPS
  NUCAPS CO2 interpolated to more sparse AIRS
  NUCAPS and AIRS are space-interpolated to TCCON stations
Quality assurance (QA)
  NUCAPS IR+MW quality flag
  AIRS trace gas quality flags
  For additional QA on NUCAPS retrievals, we also impose thresholds on retrieval degrees-of-freedom (DoF)
    CO2 = 0.8
    CO, CH4 = 0.4

## Slide 21: Carbon monoxide
NUCAPS EDR Product Performance: Ozone and Carbon Trace Gases

## Slide 22: Total Column Carbon Monoxide (CO) EDR (1/2) 17 Feb 2015 Focus Day, NUCAPS v1.5 and AIRS v6 Accepted Cases
NUCAPS v1.5
QA Yield = 62.7%
AIRS v6
NUCAPS v1.5
Preliminary

## Slide 23: Total Column Carbon Monoxide (CO) EDR (2/2) 17 Feb 2015 Focus Day, NUCAPS v1.8.3 and AIRS v6 Accepted Cases
NUCAPS v1.8.3 QA Yield = 67.7%
AIRS v6
NUCAPS v1.8.3
Preliminary

## Slide 24: NUCAPS v1.5 CO − AIRS v6 CO 17 Feb 2015 Focus Day, Accepted Cases
NUCAPS v1.5 (Nominal CrIS Resolution)
Preliminary

## Slide 25: NUCAPS v1.8.3 CO − AIRS v6 CO 17 Feb 2015 Focus Day, Accepted Cases
NUCAPS v1.8.3 (Full CrIS Resolution)
Preliminary

## Slide 26: Methane
NUCAPS EDR Product Performance: Ozone and Carbon Trace Gases

## Slide 27: Total Column Methane (CH4) EDR (1/2) 17 Feb 2015 Focus Day, NUCAPS v1.5 and AIRS v6 Accepted Cases
NUCAPS v1.5
QA Yield = 62.7%
AIRS v6
NUCAPS v1.5
Preliminary

## Slide 28: Total Column Methane (CH4) EDR (2/2) 17 Feb 2015 Focus Day, NUCAPS v1.8.3 and AIRS v6 Accepted Cases
NUCAPS v1.8.3 QA Yield = 67.7%
AIRS v6
NUCAPS v1.8.3
Preliminary

## Slide 29: NUCAPS v1.5 CH4 − AIRS v6 CH4 17 Feb 2015 Focus Day, Accepted Cases
NUCAPS v1.5 (Nominal CrIS Resolution)
Preliminary

## Slide 30: NUCAPS v1.8.3 CH4 − AIRS v6 CH4 17 Feb 2015 Focus Day, Accepted Cases
NUCAPS v1.8.3 (Full CrIS Resolution)
Preliminary

## Slide 31: Carbon Dioxide
NUCAPS EDR Product Performance: Ozone and Carbon Trace Gases

## Slide 32: Mean Column Carbon Dioxide (CO2) EDR (1/2) 17 Feb 2015 Focus Day, NUCAPS v1.5 and AIRS v6 Accepted Cases
NUCAPS v1.5
QA Yield = 29.5%
Preliminary
AIRS v6
NUCAPS v1.5

## Slide 33: Mean Column Carbon Dioxide (CO2) EDR (1/2) 17 Feb 2015 Focus Day, NUCAPS v1.8.3 and AIRS v6 Accepted Cases
NUCAPS v1.8.3
QA Yield = 39.4%
Preliminary
AIRS v6
NUCAPS v1.8.3

## Slide 34: NUCAPS v1.5 CO2 − AIRS v6 CO2 17 Feb 2015 Focus Day, NUCAPS and AIRS Accepted Cases
Preliminary
NUCAPS v1.5 (Nominal CrIS Resolution)

## Slide 35: NUCAPS v1.8.3 CO2 − AIRS v6 CO2 17 Feb 2015 Focus Day, NUCAPS and AIRS Accepted Cases
Preliminary
NUCAPS v1.8.3 (Full CrIS Resolution)

## Slide 36: NUCAPS v1.8.3 & AIRS versus TCCON: Histograms (QA cases, n = 1230)

## Slide 37: NUCAPS & AIRS versus TCCON: Summary Stats (QA cases, n = 1230)
 | v1.5 CrIS Nom Res |  |  | v1.8.3 CrIS Full Res |  |  | v6 AIRS |  | 
Trace Gas EDR | BIAS (%) | STD (%) | RMS (%) | BIAS (%) | STD (%) | RMS (%) | BIAS (%) | STD (%) | RMS (%)
CO | +5.7 (±25.0) | 24.5 (35.0) | 25.2 | −1.7 (±5.0) | 9.2 (15.0) | 9.3 | −1.5 | 7.4 | 7.6
CO2 | 0.7 (±1.0) | 1.0 (0.5) | 1.2 | −0.1 (±1.0) | 0.8 (0.5) | 0.8 | −0.6 | 1.2 | 1.4
CH4 | −8.1 (±1.0) | 1.7 (0.5) | 8.3 | −5.7 (±1.0) | 1.7 (0.5) | 6.0 | −4.1 | 1.7 | 4.4

## Slide 38: O3, CO, CH4, CO2 Trace Gas Summary
The operational NUCAPS IR ozone (O3) profile EDR products meet JPSS Level 1 requirements and have reached “Validated Maturity”
  Offline v1.5 (operational emulation, nominal CrIS resolution) meets requirements, based upon coarse/broad layer statistical analyses versus
    Collocated global ozonesondes, including dedicated ozonesondes (Validation Hierarchy Method #4)
    Global Focus Day (17 February 2015) ECMWF output (Validation Hierarchy Method #1)
  Offline v1.8.1 (full CrIS resolution) also meets Level 1 requirements based upon coarse/broad layer statistical analyses versus global Focus Day ECMWF
    Statistics are comparable to the ozonesonde-validated NUCAPS v1.5
Preliminary validation of NUCAPS carbon trace gas EDRs was based upon truth datasets:
  Collocated AIRS v6 (satellite EDR Intercomparisons, Validation Method #2)
    AIRS flown on Aqua is in the same orbit as SNPP and is thus ideal for collocations with SNPP
    Global coverage
  TCCON ground-based uplooking FTS measurements
    Spot checks of both NUCAPS and AIRS
  NUCAPS v1.8.3 CO, CH4, and CO2 versus AIRS and TCCON are reasonably close to JPSS Level 1 requirements
Future Work
  Further optimization of NUCAPS full-resolution algorithm: Implement full-res RTA delivered by UMBC
  Apply additional techniques for QA (e.g., χ2, applying AKs, etc.)
  Use TCCON H2O (provided by D. Wunch for subsample of stations) to verify conversion scheme using NUCAPS H2O
  Perform additional “spot-checks” of AIRS and NUCAPS EDRs using additional in situ datasets of opportunity
  Utilize a larger data sample (e.g., multiple focus days)

## Slide 39: Thank you! Questions?
NUCAPS EDR Product Performance: Ozone and Carbon Trace Gases