## Slide 1
Uncertainty Estimates for
NUCAPS, NASA AIRS and EUMETSAT IASI Soundings
Using
GCOS Reference Upper Air Network (GRUAN) Radiosonde
Tony Reale1
Bomin Sun2, Michael Pettey2 and Ryan Smith2
1NOAA / NESDIS /STAR
2IMSG Corporation
Joint AMS/NOAA EUMETSAT Satellite Conference
Boston, MA.
Oct. 4th, 2019

## Slide 2
Outline
    NPROVS / GRUAN
    GRUAN Uncertainty Measurement (GUM) Concept
    GUM application in Sounding product Cal/Val
    Results
    Summary

## Slide 3
25

## Slide 4
Global Climate Observing System (GCOS) Reference Upper Air Network
(GRUAN)
JPSS Dedicated RAOB
  DOE ARM (SGP, NSA, ENA)
    SSEC/Madison …
    (2) per week
    dual vs single, etc
  AEROSE
  CALWATER
  El Nino Rapid Response
  RIVAL (DOE funded)
Ongoing coordination with “other” field experiments
  Sterling Test Site
  ARM Mobile Sites
  CIRA/CSU
GRUAN & JPSS-funded Dedicated RAOBs: NPROVS Special
GRUAN
GRUAN provides fully characterized (uncertainty) Temp and RH profiles; Vaisala RS92, v2
25 Sites
15 Ref Raob

## Slide 5
Collocation GRUAN radiosonde and satellite (and nwp) observations
available in NPROVS Special and VALAR
25,000+ since 2013

## Slide 6
        ABS (m1 – m2) < k (s2 + u12 + u22)1/2
Reference Quality Upper-Air Measurements: guidance for developing GRUAN data products.,
F. J. Immler, J. Dykema, T. Gardiner, D. N. Whiteman, P. W. Thorne and H. Vomel1
Atmos. Meas. Tech.: 9 September 2010
(m1, m2) are Satellite, GRUAN geophysical profiles,
(u1, u2) the associated satellite and GRUAN uncertainty and
“s” the uncertainty due to mismatch ... “time-alias”
Strategy
GRUAN Uncertainty Measurement
(GUM)

## Slide 7
Consider two independent measurements m1 and m2 of the same measurand with standard uncertainties
u1, and u2, respectively. Assuming that the hypothesis that m1 =m2 is true and that the uncertainty (u) is normally distributed, the probability that
|m1−m2| > k (u1**2 + u2**2)1/2
occurs only by chance, is roughly 4.5% for k =2 and 0.27% for k =3.
In statistical terms, if Eq. is true for k =2, the null hypothesis that m1 = m2 can be rejected at a significance level (risk) of 4.5%; it is very likely that the two measurements did not measure the same thing, probably due to some unrecognized or unaccounted for systematic effect; “s”. We suggest to call data in this case “significantly different” and if Eq. (6) holds for k =3 (0.27% risk ) “inconsistent”.
If the results agree within k =1
|m1−m2|<k ·(s2 + u1**2 + u2**2)1/2
the data are “consistent”
and within k =2 they are “in statistical agreement” … a reasonable target for satellite sounding !
CONCEPT
Null hypothesis:
(in a statistical test) the hypothesis that there is no significant difference between specified populations, any observed difference being due to sampling or experimental error.

## Slide 8
2) Since s and u1 are “unknown” they are initially set to zero and “k0” is defined:
“k0” = ABS (m1 – m2) / u2 … initial condition
u2 k0 ~ ABS (m1 – m2) = kx (s2 + u12 + u22)1/2 … “kx” denotes some target value
s2 + u12 = ((“k0”/kx)2 –1) (u2)2
Substituting kx = 2 (“statistical agreement” with GRUAN) and ignoring the “s ”term (small …)
(for derived soundings, “s” relatively small compared to inherent error signal)
u1 = ((k0/ 2)2 –1)1/2 (u2) … uncertainty needed for “statistical agreement” with GRUAN
“u1” provides “high” estimate for the satellite product uncertainty since it includes “s“ … ?
Strategy

## Slide 9
Moisture
GRUAN Uncertainty defined in terms of Relative Humidity (RH)
Satellite sensors measure H20 vapour molecules / mixing ratio (MR)
RH uncertainty is converted MR uncertainty …
u2(MR) = u2 (RH) x Saturation (MR)
(at 300K, Saturation MR approximately 25 g/kg)
The impact of respective uncertainty in temperature (and pressure) is not included as it is “relatively” small:
At 300K (saturation MR 25g/kg), 1013 hPa, and “typical” GRUAN uncertainty values of 0.2K, 0.5 hPa and 3% RH,
MR uncertainty is estimated as 0.67 +/- 0.01 g/kg (or +/- 1.5%) … impact tends to decrease with height
(satellite sensor sensitivity to atmospheric water vapour 20 (to 40) ppm)
Strategy

## Slide 10
Enterprise Assessment
Comparing / assessing EDR products suites against the same “truth” … GRUAN reference radiosonde
    Versus same radiosonde
    Using same target “k” … uncertainty

## Slide 11
Typical distribution of collocated AIRS (v6) and NUCAPS (v5) with GRUAN Radiosonde
(+/- 6hr (right), +/- 2hr (left); 50km)
629 1519

## Slide 12
6 hour
6 hour
Collocated AIRS (v6) and NUCAPS (v5) with GRUAN Radiosonde

## Slide 13
2 hour
2 hour
Collocated AIRS (v6) and NUCAPS (v5) with GRUAN Radiosonde
1.0 1.1 0.3 (K)
0.6 0.7 0.4 (g/kg)

## Slide 14
“k0” profiles
and
expected uncertainty estimates
for
Soundings, NWP
(+/- 2 hr; 50km)

## Slide 15
0.6 0.6 0.5
0.5 0.8 0.2
0.4 0.5 0.2
0.5 0.6 0.3
0.9 1.1 0.4
u1 = ((k0/ 2)2 –1)1/2 (u2)
k0
kx
2
Collocated NUCAPS (NPP, v5), AIRS (v6) and ECMWF soundings with GRUAN Radiosonde
(+/- 2hour, 50km; IR+MW))
uncertainty
GRUAN uncertainty
mean u2 (k)
from RMS
1.0 1.1 0.3 (K)
Sept. 1, 2015 to Sept. 30, 2016)

## Slide 16
u1 = ((k0/ 2)2 –1)1/2 (u2)
k0
kx
2
0.5 0.5 0.4
0.6 0.7 0.2
0.4 0.4 0.2
0.5 0.6 0.3
0.6 0.9 0.3
Collocated NUCAPS (v5), EUMETSAT MetOp-B (v6.2) and ECMWF soundings with GRUAN Radiosonde
(+/- 2hour, 50km)
uncertainty
June 1, 2016 to March 1, 2018

## Slide 17
.01 .02 .01
.07 .08 .03
.43 .53 .20
.54 .44 ---
u1 = ((k0/ 2)2 –1)1/2 (u2)
0.11
0.52
2.26
4.99
Mean
(g/kg)
kx
2
Collocated NUCAPS (NPP, v5), AIRS (v6) and ECMWF soundings with GRUAN Radiosonde
(+/- 2hour, 50km; IR+MW))
uncertainty
GRUAN uncertainty
mean u2 (g/kg)
from RMS
0.6 0.7 0.4 (K)

## Slide 18
.01 .02 .01
.10 .11 .05
.46 .72 .28
.10 .31 ---
u1 = ((k0/ 2)2 –1)1/2 (u2)
0.16
0.66
2.99
7.14
Mean
(g/kg)
kx
2
Collocated NUCAPS (v5), EUMETSAT MetOp-B (v6.2) and ECMWF soundings with GRUAN Radiosonde
(+/- 2hour, 50km)
uncertainty

## Slide 19
NUCAPS Users (AWIPS-2)
NOAA Unique Combined Atmospheric Processing System (NUCAPS) sounding products are distributed to NWS forecast users in the field via the NOAA NWS Advanced Weather Information Processing System (AWIPS-2)
The ARM/GRUAN SGP (Oklahoma) site is a strategic location in the context of NOAA NWS AWIPS-2) forecast users …
Having estimates of “expected uncertainties of NUCAPS soundings (IR +MW pass QC) at SGP based on GRUAN reference radiosondes has potential value …

## Slide 20
SGP is strategic assessment site for NWS AWIPS-2 users of NUCAPS …
(315m … 945 to 972 hPa)

## Slide 21
kx
2
k0
u1 = ((k0/ 2)2 –1)1/2 (u2)
0.7 0.7 0.5
0.4 0.6 0.2
0.3 0.4 0.3
0.5 0.6 0.3
0.8 1.0 0.5
GRUAN
Temperature
Uncertainty u2
Collocated NUCAPS (NPP, v5) and AIRS (v6) soundings with SGP Radiosonde
(+/- 2hour, 50km; IR+MW))
uncertainty

## Slide 22
kx
2
k0
u1 = ((k0/ 2)2 –1)1/2 (u2)
0.7 0.8 0.4
0.4 0.5 0.1
0.4 0.5 0.2
0.5 0.6 0.2
0.8 1.0 0.4
GRUAN
Temperature
Uncertainty u2
uncertainty
Collocated NUCAPS (v5), EUMETSAT MetOp-B (v6.2) and ECMWF soundings with SGP Radiosonde
(+/- 2hour, 50km)

## Slide 23
kx
2
k0
u1 = ((k0/ 2)2 –1)1/2 (u2)
.01 .01 .01
.11 .12 .07
.65 .88 .30
.48 .60 .10
GRUAN
H20 Vapor
Uncertainty u2
0.20
0.72
3.93
3.19
Mean
(g/kg)
uncertainty
Collocated NUCAPS (NPP, v5) and AIRS (v6) soundings with SGP Radiosonde
(+/- 2hour, 50km; IR+MW))

## Slide 24
kx
2
.02 .04 .01
.11 .14 .05
.50 .67 .25
.42 1.0 ---
u1 = ((k0/ 2)2 –1)1/2 (u2)
GRUAN
H20 Vapor
Uncertainty u2
k0
0.25
0.86
4.05
4.61
Mean
(g/kg)
uncertainty
Collocated NUCAPS (v5), EUMETSAT MetOp-B (v6.2) and ECMWF soundings with SGP Radiosonde
(+/- 2hour, 50km)

## Slide 25
Collocated NUCAPS (v5), EUMETSAT MetOp-B (v6.2) and ECMWF soundings with SGP Radiosonde
(+/- 2hour, 50km)

## Slide 26
Summary / Forward
    NPROVS Special Dataset w/GRUAN pivotal for NOAA Cal/Val for soundings …
      JPSS are GRUAN Users!
    Uncertainty Application Strategy for geophysical sounding products presented
    Strategy tested for respective “optimal” periods for 1) NUCAPS NPP vs AIRS and 2) NUCAPS versus EUMETSAT MetOp-B
    Expected uncertainty estimates for soundings correlated with RMS but appear low (particularly Temp)
    Expected uncertainty estimates at SGP relevant for NUCAPS Users via NWS AWIPS-2 and Provider …
    Update results using GRUAN RS41 and latest Sounding products
    Radiance Space…. GSICS; RT model and Satellite Sensor assessment
    Publication …

## Slide 27
GRUAN ICM-19, Singapore, May 2019

## Slide 28
Collocated NUCAPS (NPP, v5) and AIRS (v6) soundings with GRUAN Radiosonde
(+/- 2hour, 50km; IR+MW)
see slides 14 vs 20
All GRUAN
SGP
Sdev lower